Hcal DAQ Update
Scott Barcus
2/7/2020

---
TDC Timing Resolution
- Require 3 tubes vertically in coincidence to fire.
- Reference time is the average of the TDC times of the top and bottom tubes.
- Require surrounding 6 tubes not to have fired.
- Red timing resolution σ1:
  - TDC time – TDC reference
- Blue timing resolution σ2:
  - Reference resolution (Top TDC -Bottom TDC)
- Want timing resolution of only center PMT σ3.
  - σ12 = σ22 + σ32

---
TDC Timing Resolution Run 701 (Modules 12-23)

---
TDC Timing Resolution Run 706 (Modules 12-23)

---
TDC Timing Resolution Run 706 (Modules 120-131)

---
fADC Time Walk Corrections
- Define time over threshold for fADC times.
  - ¼ average fADC peak height.
  - Landau fit to fADC pulses.
- Bigger fADC pulses cross threshold earlier.
  - Want to correct for this time walk.
- Plot fADC integral vs time over threshold.
  - Fit this spectrum. f(fADC integral)
  - Using a sum of an exponential and a log.
    - Probably could simplify this.
- Correct raw fADC times as follows (blue plots):
  - Raw time over threshold – f(fADC integral)

---
Landau Fit to fADC Signal

---
Time Walk for 706 (mods 12-23)

---
fADC Timing Resolutions (Corrected and Uncorrected) Run 706 (mods 12-23)

---
706 Time Walk Cont.
- Time walk corrections (blue) slightly improve resolution.
- JLab tubes and far right tubes see very little rate.
- Go back and use same reference time method used for the TDC times with fADC times.
- Need resolutions of 0.5 ns for GEn.
  - Just single TDC resolution?
  - Can add stricter cuts for verticallity etc.
  - Want to combine TDC and fADC for better timing resolution.
    - Plot TDC time – fADC time for time walk and correct for combined result?

---
706 Number of Photoelectrons
- Calibrate HV to create distinct SPE peak.
  - Fit SPE peak with a Gaussian.
  - NPE = (Avg fADC height/StdDev fADC height)^2

---
NPE Cont.
Module	Avg. NPE	rChi^2 of Fit	Visual Fit Quality
0	6.31	0.84	Good
1	5.86	0.89	Decent
2	15.49	0.89	Decent
3	10.42	0.69	Decent
4	13.5	0.81	Decent
5	8.91	1.33	Good
6	0.34	6.09	Bad
7	12.68	1.30	Decent
- Need to improve fits (maybe adjust HV again).
- JLab tubes can't separate SPE peak.
  - HV max -2200 V.
- Compare with G4SBS cosmic results.